## Slide 1: Lec 7: Systems and Classification of Systems
Dr. Arsla Khan

## Slide 2: System
A system may be defined as a set of elements or functional blocks which are connected together and produces an output in response to the input signal.
Let and be the input and output signals, respectively of a system. Then system is viewed as transformation (or mapping) of into .
It is represented as where is defined as some well defined rule to transform the into .

## Slide 3: Types of Systems
Continuous Time System
    Systems in which input and output, both signals are continuous in nature.
    e.g. Audio and video amplifier, power supplies etc
Discrete Time System
    Systems in which input and output, both signals are discrete in nature.
    e.g. microprocessors, shift registers

## Slide 4: Interconnection of Systems
Systems can be interconnected in multiple ways
    1) Series(Cascaded) Interconnection
        Output of system 1 is input of other system
        Overall impulse response is equal to convolution of individual impulse responses.

## Slide 5
2) Parallel Interconnection
    Same input is applied to all systems.
    Overall impulse response is equal to addition of individual impulse responses
3) Series/Parallel Interconnection
    Combination of series and parallel combination

## Slide 6
4) Feedback Interconnection
    Output of system 1 is the input to system 2, while the output of system 2 is fed back and added to the external input to produce the actual input to system 1.

## Slide 7: Exp 7.1: Write relationship between input and output signals
Multiple input by 2 
Square of input 
Relationship is:

## Slide 8: Classification of Systems
i) Causal Systems and Non-causal Systems
ii) Static Systems and Dynamic Systems
iii) Time-invariant Systems and Time-variant Systems
iv) Stable Systems and Unstable Systems
v) Linear Systems and Non-linear Systems
vi) Invertible Systems and Inverse Systems

## Slide 9: 1) Causal and Non-Causal Systems
A system is said to be causal if the response or output does not begin before the input function is applied.
In other words,
    Response of the causal system to an input does not depend on future values of that input but depends only on the present and past values of the input.

## Slide 10
(i)
Solution:
Put different values of in above equation to check whether it is causal or not
    Put
    Put
    Put
is depending on previous and present values of only so it is a causal system
Exp 7.2: Determine whether the systems are causal or non-causal
Present value of input
Past value of input

## Slide 11
(ii)
Solution:
Put different values of in above equation to check whether it is causal or not
    Put
    Put
    Put
is depending on future values of only so it is a non-causal system
Future value of input
Future value of input
Future value of input

## Slide 12
(iii)
Solution:
Put different values of in above equation to check whether it is causal or not
    Put
    Put
    Put
is depending on present values of only so it is a causal system
present value of input
present value of input
present value of input

## Slide 13
(iv)
Solution:
Put different values of in above equation to check whether it is causal or not
    Put
    Put
    Put
is depending on present and future values of only so it is a non-causal system

## Slide 14
(v)
Solution:
Put different values of in above equation to check whether it is causal or not
    Put
    Put
    Put
is depending on previous values of only so it is a causal system

## Slide 15
Static systems are also known as memoryless systems
Static systems contain no storage elements (thus, no integrals, derivatives or signal delays)
A static or memoryless system is a system with an output signal whose values depends upon the present value of the input signal only. Otherwise the system is dynamic or with memory.
2) Static (memoryless) and Dynamic (with memory) Systems

## Slide 16
Exp 7.3: Determine whether the systems are static or dynamic
(i)
Solution:
Put different values of in above equation to check whether it is static or not
    Put
    Put
    Put
is depending on present values of only so it is a static system

## Slide 17
(ii)
Solution:
Put different values of in above equation to check whether it is static or not
    Put
    Put
    Put
is depending on previous and present of values only so it is a dynamic system

## Slide 18
(ii)
Solution:
Put different values of in above equation to check whether it is static or not
    Put
    Put
    Put
is depending on previous and present of values only so it is a dynamic system

## Slide 19
A system is time invariant if the time shift in the input signal results in corresponding time shift in the output.
Let i.e. is response of
Then if is delayed by time then output will also be delayed by the same time. i.e.
3) Time Invariant and Time Variant Systems

## Slide 20
Sr. # | Operation or system | Type
1 | Bus and train arrival and departure times | Time Invariant
2 | Rainfall per month | Time variant
3 | Thermal noise in components | Time variant
4 | Noise effects in radio communication | Time variant
5 | File handling in C language | Time invariant
6 | Printing documents by printer | Time invariant
Time invariant systems are independent of time/day/year whereas time variant systems are effected at which time you are analyzing the system.

## Slide 21: Steps to test for time invariance property
Step 1: First delay the input by i.e. and then pass it through the system
Step 2: Then delay the output itself by i.e.
Step 3: Now compare both outputs. If
     Time variant
     Time invariant

## Slide 22
Shifting
System
System
System
R.H.S
L.H.S

## Slide 23
Step 1: First delay the input by i.e. and then pass it through the system
Step 2: Now delay the output by . Hence we have to replace by
Step 3: Compare with
Both are same so system is time invariant
Exp 7.4: Determine whether the systems are time invariant or time variant

## Slide 24
Step 1: First delay the input by i.e. and then pass it through the system
Step 2: Now delay the output by . Hence we have to replace by
Step 3: Compare with
Both are not same so system is time variant

## Slide 25
Step 1: Determine the output for delayed input i.e. .
Step 2: Now delay the output by . Hence we have to replace by
Step 3: Compare with
Both are not same so system is time variant

## Slide 26
Step 1: Determine the output for delayed input i.e. .
Step 2: Now delay the output by . Hence we have to replace by
Step 3: Compare with
Both are same so system is time invariant

## Slide 27
Step 1: Determine the output for delayed input i.e. .
Step 2: Now delay the output by . Hence we have to replace by
Step 3: Compare with
Both are not same so system is time variant

## Slide 28: Thank You !!!